## Slide 1: Smart Milk Spoilage Experiment
Nahom Abera, Kamrul Tarafder, Diana Avila

## Slide 2: Introduction
Background:
  Milk is a perishable product that requires proper storage to prevent spoilage.
  Understanding the impact of temperature on milk spoilage can guide storage practices and reduce waste.
Context:
  This experiment simulates two common storage conditions, refrigerated and room temperature, to analyze spoilage progression.
Importance:
  Insights from this study can inform consumer behavior, optimize storage conditions, and enhance food safety.

## Slide 3: Objective
Purpose:
  To evaluate how temperature influences the spoilage of milk over time.Key
Questions:
  How does temperature vary in refrigerated and unrefrigerated conditions over time?
  How does spoilage progression differ between the two storage setups?

## Slide 4: Experimental Setup
Setups: One Milk stored in a refrigerator and another Milk stored at room temperature.
Hardware: Raspberry Pi, ESP32, Temperature Sensor and Camera.
Software: Python, C++, Arduino IDE
Additional Evaluation: Smell both milk samples twice daily and record observations.
Timeframe: 2 weeks.
Storage Conditions:
  Refrigerated Milk: Maintained at 38 – 40°F.
  Unrefrigerated Milk: Exposed to room temperature 67 - 70°F.

## Slide 5: Hardware Setup

## Slide 6: Methodology
Temperature Measurement Setup:
  The unrefrigerated milk's temperature was monitored using a MYOSA BMP sensor connected to a MYOSA board, which was interfaced with a Raspberry Pi.
  The BMP sensor measured temperature in both Fahrenheit (°F) and Celsius (°C).
  Temperature data was recorded every five minutes by the Raspberry Pi and stored in an organized log file for later analysis.
Image Capture Setup:
  The Raspberry Pi was equipped with a camera module to capture images of the unrefrigerated milk at regular intervals. Pictures were taken every five minutes during the monitoring process.
  For the refrigerated setup, images of both the refrigerated and unrefrigerated milk were captured twice daily using a phone camera.
Smell Test and Manual Data Collection:
  Twice daily, a smell test was conducted for both setups:
    Refrigerated Milk: The smell was assessed and classified into categories (e.g., "Fresh," "Slightly Sour," "Noticeably Sour," "Sour/Spoiled").
    Unrefrigerated Milk: Similarly, the smell was categorized based on the same criteria.
  Simultaneously, temperature readings from:
    The refrigerator's cooler for the refrigerated milk.
    The BMP sensor for the unrefrigerated milk.
  These measurements, along with the smell classification, were manually recorded in an Excel sheet.

## Slide 7: Analysis
Refrigerated Milk:
  Consistent temperature range (~38–40°F).
  No significant spoilage observed during the experiment.
Unrefrigerated Milk:
  Gradual increase in spoilage levels with time.
  Temperature fluctuated between 67°F and 70°F
Temperature Trends:
  Refrigerated milk maintained a stable temperature, preventing spoilage.
  Unrefrigerated milk experienced slight fluctuations but remained within a high range conducive to bacterial growth.
Impact on Spoilage:
  Unrefrigerated milk began to spoil within the first 24 hours, transitioning from "Fresh" to "Slightly Sour“ and then becoming “Noticeably Sour” and “Sour/Spoiled” in just four days.
  Refrigerated milk showed no spoilage throughout the experiment until the sixth day in which it smell changed from “Fresh” to “Slightly Sour.”

## Slide 8: Graphs and Visualizations
Unrefrigerated Milk Temperature Over Time
Refrigerated Milk Temperature Over Time

## Slide 9: Graphs and Visualizations
Unrefrigerated Milk Spoilage Progression Over Time (Smell Score)
Refrigerated Milk Spoilage Progression Over Time (Smell Score)

## Slide 10: Graphs and Visualizations
Unrefrigerated Milk Temperature and Spoilage Over Time

## Slide 11: Results
Unrefrigerated Milk:
  The data shows that milk stored at room temperature began to exhibit signs of spoilage within approximately one to two days, transitioning from “Fresh” to “Slightly Sour” and then becoming “Noticeably Sour.”
  By December 3rd, the unrefrigerated milk had reached a clearly “Sour/Spoiled” state, as confirmed by both smell tests and visual evidence (images showing curdling or discoloration).
  The relatively high temperature (~68°F) accelerated bacterial growth and fermentation processes which led to rapid spoiling process.
Refrigerated Milk:
  The refrigerated milk’s temperature remained around 38°F, significantly slowing bacterial growth.
  Over the same time period, the refrigerated sample remained “Fresh” for most of the observation window, with only a very slight sourness developing after six days.
  This difference in the spoilage rate underscores the importance of proper refrigeration.
Key Observations:
  Higher storage temperatures strongly link with faster spoilage.
  Milk at proper refrigeration temperatures stays fresher for longer, delaying both sensory (smell-based) and visual signs of spoilage.
  The spoilage date (December 3rd) for the unrefrigerated milk provides a clear benchmark for how quickly milk can degrade without temperature control.

## Slide 12: Summary
This experiment demonstrates the direct impact of temperature on milk spoilage. The unrefrigerated milk, maintained at approximately 68°F, transitioned from fresh to spoiled within three days which illustrates a rapid decline in quality. In contrast, the refrigerated milk remained fresh much longer under stable, cold conditions (around 38°F), showing significantly delayed spoilage onset.
These findings support standard food safety guidelines which highlight maintaining proper refrigeration is vital to extending the shelf life of dairy products. The combination of quantitative (temperature logs, smell scores) and qualitative (visual inspection, descriptive smell tests) approaches offers a comprehensive understanding of spoilage dynamics in different environmental conditions.

## Slide 13: Thanks!